## Slide 1
Agriculture Plot Analysis
Done By:
Sundar R - S20220010215
Kache Nivas - S20220010092
01

## Slide 2
02
GIS-Based Agricultural Decision Support
  Rapid urbanization and climate change are affecting agricultural productivity.
  Farmers need decision-making tools for selecting optimal plots and infrastructure planning.
  GIS offers spatial insights through multi-layered analysis.
  This project focuses on helping farmers in Yelahanka(North Bengaluru) and Sarjapur(South Bengaluru) identify the best land for thier specific needs.

## Slide 3
03
Problem Statement & Goals
Problem:
Farmers lack spatial tools to evaluate plot suitability and other parameters for decision making.
Objectives:
  Identify suitable plots for cultivation based on environmental and soil conditions.
  Determine shortest access routes from plots to other amenities using road network analysis.
  Develop a methodology that is replicable and scalable for various other crops and parameters

## Slide 4
04
Study Area: Yelahanka and Sarjapur
Yelahanka:
  A rapidly developing peri-urban region in North Bangalore, known for a mix of residential zones, agricultural activity, and expanding infrastructure.
Sarjapur:
  A peri-urban region with diverse terrain, road networks, and active agriculture.
Datasets Used:
  Satellite Imagery
  Temperature, Elevation, Slope, Air Quality(raster)
  Land Plots, Forest, Waste Dumping Land, Water Bodies, Residential Complex(polygon)
  Market Access, Farmer Education center, AgroHub Industries, Co-op Banks, Hospitals(point)
  Roads (line)

## Slide 5
05
YELAHANKA(NORTH BENGALURU)

## Slide 6
06
SARJAPUR(SOUTH BENGALURU)

## Slide 7
Data Collection & Preprocessing
07
Workflow Diagram
Vector-Based Filtering
Raster Preparation & Normalization
Vector and Raster Analysis
Proximity & Accessibility Analysis
Result Visualization & Map Output

## Slide 8
08
Data Acquisition & Preparation
  Data Sources: Vector layers were digitized using satellite imagery from Bhuvan manually
  Attribute Enhancement: Soil Type was manually added to attribute Table.
  Layers Used & Purpose:
  Agro Hub Industry (point): Agricultural processing and support
  Residential Complex (polygon): Avoid urban-agriculture conflict
  Hospitals (point): Emergency access planning
  Forest (polygon): Avoid restricted/sensitive zones
How are Vector Layers Obtained?

## Slide 9
09
Data Acquisition & Preparation
Layers Used & Purpose:
  Water Bodies (polygon): Assess irrigation potential
  Market (point): Access to agri-supply chains
  Waste Dumping Land (polygon): Excluded from analysis
  Land Parcels (polygon): Base layer for suitability checks
  Cooperative Banks (point): Access to financial services
  Roads (line): Connectivity and routing
  Farming Education Centers (point): Farmer knowledge access

## Slide 10
10
Data Acquisition & Preparation
  Data Sources:
  Raster layers sourced from remote sensing platforms like SRTM via Google Earth Engine.
  Preprocessing:
  Reprojected to common CRS
  Clipped to study area
  Standardized pixel resolution
  Layers & Purpose:
  NO₂ (Air Quality): Assess pollution impact on crops
  Elevation: Terrain analysis, slope derivation
  Slope: Water retention, machinery access
  Temperature: Crop growth & heat stress zones
How Raster Layers are Obtained?

## Slide 11
11
Queries & Logic: Yelahanka
Query 1(Vector): Identify areas suitable for establishing a new agro-processing industry, ensuring they are close to key facilities but far from environmentally sensitive zones
Method:
  Buffer Creation:
  Create a 2 km buffer around roads and agro-industries.
  Create a negative buffer (500 m) around water bodies, forests, and residential areas to exclude them.
  Overlay Analysis:
  Intersect the positive buffers with the land layer to find potential areas.
  Erase regions overlapping with negative buffers.
  Final Selection:
The resulting polygons indicate the most suitable locations for setting up new facilities.

## Slide 12
12
Intersection of Buffered Roads and Agro-Industries with Land
Positive Buffer
Forest Buffer
Water Buffer

## Slide 13
13
Buffer Residential
Negative Buffer
Result

## Slide 14
14
Queries & Logic: Yelahanka
Query 2 (Vector):
Determine the fastest route from a market to an agro-processing industry.
Method:
Network Preparation:
Ensure the road network has a travel_time field (in minutes), calculated using length and assigned speed.
Shortest Path Analysis:
Use the Shortest Path (Point to Point) tool in QGIS:
  Start Point: Market location
  End Point: Agro-Industry location
  Cost Field: travel_time
Result:
The output line shows the fastest travel route along the road network, based on the travel time field.

## Slide 15
15
Attribute Table
Market
Co-op Bank

## Slide 16
16
Roads with constraints
Result

## Slide 17
17
Queries & Logic: Yelahanka
Query 3 (Raster + Vector):
Identify zones suitable for prolonged agriculture with low NO₂ levels and favorable cool temperatures.
Method:
  Reclassify Rasters:
    NO₂: Low = 1 (suitable), Medium–High = 0
    Temperature: Cool–Moderate = 1, High = 0
  Overlay using Raster Calculator:
  Reclass_NO2 * Reclass_Temp
    Output 1 indicates optimal conditions(0.6*No2 + 0.4*Temp).
  Mask with Land Vector Layer:
    Use “Clip Raster by Mask Layer” to retain only land areas.
Result:
Final output shows land parcels ideal for long-term agriculture under clean air and favorable temperature zones.

## Slide 18
18
Air Quality No2
AirQuality-Normalized
Temperature
Temperature-Normalized

## Slide 19
19
Required - Raster with Land
Output Layer

## Slide 20
20
Queries & Logic: Sarjapur
Query 1 (Raster + Vector):
Identify optimal plots for cotton cultivation using soil and environmental factors.
Method:
  Filter by Soil Type:
    Select and export plots with black soil from the land parcel layer.
  Raster Overlay:
    Use Slope, Elevation, and Temperature rasters.
    Normalize each raster to a 0–1 scale.
  Calculate Suitability (Raster Calculator):
  Cotton Suitability = (0.3 × Slope_norm) + (0.2 × Elevation_norm) + (0.5 × Temp_norm)
  Final Masking:
    Clip the Suitability Raster using the black soil vector layer.
Result:
  Output highlights suitable zones for cotton within black soil regions based on environmental parameters.

## Slide 21
Cotton_Suitability_
Index
Final output with the suitability index overlayed over black soil land plots
All available Land Plots
Plots with only Black Soil
21

## Slide 22
22
Queries & Logic: Sarjapur
Query 2 (Vector):
Find ideal locations for farmer housing based on proximity to amenities and avoidance of unsuitable areas.
Method:
  Buffer 200m around:
    Negative features: Residential areas, dumps, water bodies → Union → Negative Zone
    Positive features: Roads, hospitals, land plots, markets → Union → Positive Zone
  Final Output:
  Suitable Area = Positive Zone - Negative Zone
Result:
Optimally located housing zones with access to amenities and minimal risks.

## Slide 23
Positive Buffer
Both Layers Overlayed
Negative Buffer
After difference
23

## Slide 24
24
Queries & Logic: Sarjapur
Query 3 (Vector):
Identify land plots with best road access for efficient produce transportation.
Method:
Buffer 200m around:
Road network → Road_Buffer
Select by location:
From Land_Plots that intersect Road_Buffer → Selected_Plots
Final Output:
Selected_Plots within 200m of roads
Result:
Land plots with optimal transport connectivity for agricultural produce.

## Slide 25
Road Buffer and Plots Layer
Result
25

## Slide 26
26
Queries & Logic: Sarjapur
Query 4(Vector):
Identify the shortest paths from all land plots to every market.
Method:
Reduce the polygon plot layer to it’s centroid point layer for network analysis:
Land_Plot(Polygon) → Land_Plot_Centroids(Point)
Network Analysis:
Found the shortest path to each market from individual centroid points, Using Shortest Path(point to layer) network analysis tool.
Final Output:
Merge all the obtained intermediate vector layer for each source point.
Result:
A vector layer with the shortest paths laid out from each land point to every market point.

## Slide 27
27
Land Plots and it’s centroids
Performing Network analysis on each point individually
Intermediate layer from one source plot point
Merged Final Layer

## Slide 28
28
Market Research
Market Research
Target Users
  Smallholder farmers (rural & semi-urban India)
  Agricultural officers & planners
  NGOs in rural development
  Agri-tech startups & researchers
Key Problems Identified
  No easy tools for identifying suitable agri-land
  Difficulty accessing info on proximity to markets, hospitals, water
  Data is fragmented and outdated
  Lack of digital support for crop planning

## Slide 29
Tool | Features | Limitations
AgriStack | Govt. agri-database | Limited Access, still evolving
Bhuvan Geoportal | Land use satellite maps | Lacks crop-specific/local detail
farmonaut | Crop health via remote sensing | Doesn’t suggest land/crop suitability
Google Earth Engine | Advanced spatial tools | Requires Programming Know-How
29
Market Research

## Slide 30
Thank You!
30